## Slide 1
An Instruction Offloading PIM Architecture for Deep Learning Application
Group: Yi Ling, Siyu Mou, Jiayou Jin, Hao Peng, Kunyu Wu

## Slide 2
• Today’s Content:
Background Introduction
Architecture Proposal
Presentation Overview
2
Implementation
Benchmark Comparison
Future Direction

## Slide 3
Background Introduction
2
Convolutional Neural Network (CNN) Basics
A CNN consists of multiple convolutional layers to learn the salient features and a few fully connected layers for classification
In a convolution layer, a large mount of multiply-and-accumulation (MAC) operations are taken during the computation process
Plus data needed to calculate often exceed the capacity of cache resulting in large amounts of data being read from the main memory (DRAM)

## Slide 4
Background Introduction
2
Breaking the von Neumann bottleneck
Memory bandwidth limitation: CNNs need to handle large-scale matrix operations and data transfers, which often make memory bandwidth a system bottleneck.
High latency: The latency of retrieving data from main memory (typically at the nanosecond level) can significantly impact the inference and training speed of CNNs.

## Slide 5
Architecture Proposal
2
Feature:
Instruction Offloading: Moving data intensive program to PIM cores through a custom compiler
Processing In Memory: By running program in DDRM chip, it will reduce the amount of loading and storing time of program

## Slide 6
Implementation
2
ISA Design
Custom Compiler
Architecture Simulation

## Slide 7
Implementation-ISA Design
2
Our basis: ARMv7 ISA
Register-Register: Its purpose is to perform operations on the data in the registers, usually without involving memory operations. Like: Add, Subtraction, Multiply, Division
Data Transfer: These instructions are used to load data from memory into registers, or to store data from registers into memory. Like: Load, Store.

## Slide 8
Implementation-ISA Design
Our PIM ISA:
For register-register operation
Opx (31-24): Operation extension field, specifies instruction categories or special operations.
Op (23-20): Opcode field, defines basic operations like addition, subtraction, or data movement.
Rs1 (19-16): Source register 1, the first input register.
Rd (15-12): Destination register, stores the operation result.
M (11): Mode selector, determines execution on CPU (0) or PIM-Core (1).
imm4 (10-7): 4-bit immediate value
Op2 (6-5): Auxiliary opcode, extends operation definitions.
0 (4): Reserved bit, ensures format alignment.
Rs2 (3-0): Source register 2, the second input register.
Const (10-0): Immediate constant.

## Slide 9
Implementation-ISA Design
2
Example：
ADD instruction decoding
LOAD instruction decoding

## Slide 10
Implementation-ISA Design
2
Instruction and Meaning:

## Slide 11
Implementation-Architecture Simulation
2
1. Architecture Detection:
The architecture that distinguishes instructions based on the prefix of opcodes (such as PMEM_) or specific values of fields:
If the opcode starts with PMEM_, it is a PIM instruction. Otherwise, it is an ARM instruction

## Slide 12
Implementation-Architecture Simulation
2
2. Parsing:
Input format: Assembly instructions consist of opcodes and parameters, for example:.
Parsing method:
Opcodes (such as ADD, PMEM_ADD).
The parameter list (such as R1, R2, R3,5) is further divided into individual registers or immediate numbers (R1, R2, R3, 5).

## Slide 13
Implementation-Architecture Simulation
2
3. Field Generation:
Generate corresponding fields based on the parsed instructions and architecture (ARM or PIM):
Each field has a clear position and length. Convert register numbers, immediate numbers, etc. into binary using fixed rules..
Field example (using ARM as an example):
Opx (31-28 bits): Retrieve the corresponding value from the operation code table.
Op (27-20 bits): The opcode corresponding to a specific instruction.
Rs1 (19-16 bits): Source register, converted to 4-bit binary.

## Slide 14
Implementation-Architecture Simulation
2
4. Decoding:
Decoding rule: Parse the complete instruction in binary field order, extract the value of each field, and print out the field name, binary value, and corresponding decimal value.
Field parsing method: Use binary slicing operation to extract each field:
Opx: binary[0:4]
Op: binary[4:12]
Rs1: binary[12:16]

## Slide 15
OUTPUT
2

## Slide 16
OUTPUT
2

## Slide 17
Implementation-Architecture Simulation
2
Introduction - gem5:
Host: the actual hardware you're using
Simulator: Runs on the host
  Exposes hardware to the guest
Guest: Code running on simulated hardware
  OS running on gem5 is guest OS
  gem5 is simulating hardware
Simulator's code: Runs natively
  executes/emulates the guest code
Guest's code: (or benchmark, workload, etc.)
  Runs on gem5, not on the host.

## Slide 18
Implementation-Architecture Simulation
2
Component - gem5:
- CPU
- Cache Hierarchy
Memory System
Board: The “backbone” of the system

## Slide 19
Implementation-Architecture Simulation
2
Steps of simulation:
Installing gem5
Configuring simulator & Implementation
Running Benchmark
https://www.gem5.org/
Configure the environment & install dependency packages
Configure the components from the official repository
Modify the component parameters in the config script to implementthe PIM system
Obtain benchmark resources from gem5

## Slide 20
Implementation-Architecture Simulation
2
Configuration

## Slide 21
Implementation-Architecture Simulation
2
CPU-Only Model
CPU Model: Timing CPU

## Slide 22
Implementation-Architecture Simulation
2
PIM Core Model
CPU Model: Atomic CPU
Atomic Memory Access: It is used for fast forwarding and warming up caches and return an approximate time to complete the request without any resource contention or queuing delay which is suitable to simulate DMA

## Slide 23
Benchmark Comparison
2
From gem5 resource, we choose 5 benchmark
(Graph Analysis Performance Benchmark Suite)
arm-gapbs-bfs-run:
Breadth-First Search (BFS): A search algorithm used to find the shortest path from a source node to a target node.arm-gapbs-tc-run:
Triangle Counting: Calculates the number of triangles in a graph, often used in social network analysis, etc.
NPB (NAS Parallel Benchmarks)
arm-npb-bt-size-s-run:
BT (Block Tridiagonal): Often used to solve spatiotemporal discretization problems in physics.
arm-npb-cg-size-s-run:
CG (Conjugate Gradient): A method used to solve linear systems using the conjugate gradient method.

## Slide 24
Benchmark Comparison-Matrix Multiply
2
PIM Core
CPU Only

## Slide 25
Benchmark Comparison
2
Chart: 
| PIM-Core | CPU-Only | PIM-Core | CPU-Only | npb-bt | npb-cg
SimSec | 0.40558 | 1.2066 | 0.32629 | 1.3788
Chart: SimSec
| PIM-Core | CPU-Only | PIM-Core | CPU-Only | PIM-Core | CPU-Only | gapbs-bfs | gapbs-tc | matrix-multiply
 | 0.010366 | 0.02626 | 0.048239 | 0.11694 | 0.025724 | 0.081297 | 0
Speedup(exTimePC / exTime CPU):
1. Gapbs-bfs: X2.53
2. Gapbs-tc: X2.43
3. Matrix-multiply: X3.16
4. Npb-bt: X2.98
5. Npb-cg: X4.22
Average Speedup: X3.06!!!

## Slide 26
Performance Modeling
2
Not always does the PIM core encounter a resource contention state
Not always can the PIM core offload all the task

## Slide 27
Performance Modeling
2
Amdahl’s Law:
Increasing by Amdahl’s law
Decreasing by Queuing theory
Queuing theory:

## Slide 28
Future Direction
2
Smarter compiler:
Achieving most out of PIM core through smart task offloading
Domain specific architecture for PIM Core:
Targeted acceleration by modifying the PIM core architecture to make it better suited for accelerating deep learning tasks.

## Slide 29
Contribution
2
Yi Ling: Architecture Proposal, Simulation & Analysis(50%), PPT(30%)
Jiayou Jin: Architecture Proposal, Simulation & Analysis(50%), PPT(20%)
Siyu Mou: Architecture Proposal, ISA design & Compiler(50%), PPT(20%)
Hao Peng: Architecture Proposal, ISA design & Compiler(50%), PPT(20%)
Kunyu Wu: PPT(10%)
Thanks for all group member’s commitment!